## Slide 1: Chapter 2
Instructions: Language of the Computer
Click to add text

## Slide 2: Instruction Set
The repertoire of instructions of a computer
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
Many modern computers also have simple instruction sets
§2.1 Introduction
Notes: - To command a computer’s hardware, you must speak its language. The words of a computer’s language are called instructions, and its vocabulary is called an instruction set.
- You might think that the languages of computers would be as diverse as those of people, but in reality computer languages are quite similar, more like regional dialects than like independent languages.

## Slide 3: The MIPS Instruction Set
Used as the example throughout the course
Stanford MIPS commercialized by MIPS Technologies (www.mips.com)
Large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …
Typical of many modern ISAs
  See MIPS Reference Data tear-out card, and Appendixes B and E of the textbook
Notes: three other popular instruction sets.
- ARMv7 is similar to MIPS. More than 9 billion chips with ARM processors were manufactured in 2011, making it the most popular instruction set in the world.
- The second example is the Intel x86, which powers both the PC and the cloud of the PostPC Era.
- The third example is ARMv8, which extends the address size of the ARMv7 from 32 bits to 64 bits. Ironically, as we shall see, this 2013 instruction set is closer to MIPS than it is to ARMv7.

## Slide 4: Arithmetic Operations
Add and subtract, three operands
  Two sources and one destination
add a, b, c # a gets b + c
All arithmetic operations have this form
Design Principle 1: Simplicity favours regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
§2.2 Operations of the Computer Hardware
Notes: MIPS rule: All arthematic operations (add, subtract) have three operands – no more or no less
In the addition example, three operands are a (source 1), b (source 2), and c (dest), sum of b & c is stored in ‘a’
Why not use variable number of operands?
  Design principle: Simplicity favors regularity
  Reason: conforms to the philosophy of keeping the hardware simple, hardware for a variable number of operands is more complicated than hardware for a fixed number.

## Slide 5: Arithmetic Example
C code:
f = (g + h) - (i + j);
Compiled MIPS code:
add t0, g, h # temp t0 = g + h add t1, i, j # temp t1 = i + j sub f, t0, t1 # f = t0 - t1
Notes: - The translation from C to MIPS assembly language instructions is performed by the compiler.
The compiler must break this statement into several assembly instructions, since only one operation is performed per MIPS instruction.
The first MIPS instruction calculates the sum of g and h. We must place the result somewhere, so the compiler creates a temporary variable, called t0:
add t0,g,h # temporary variable t0 contains g + h
Although the next operation is subtract, we need to calculate the sum of i and j before we can subtract.
  Thus, the second instruction places the sum of i and j in another temporary variable created by the compiler, called t1:
add t1,i,j # temporary variable t1 contains i + j
- Finally, the subtract instruction subtracts the second sum from the first and places the difference in the variable f, completing the compiled code:
sub f,t0,t1 # f gets t0 – t1, which is (g + h) – (i + j)

## Slide 6: Register Operands
Arithmetic instructions use register operands
MIPS has a 32 × 32-bit register file
  Use for frequently accessed data
  Numbered 0 to 31
  32-bit data called a “word”
Assembler names
  $t0, $t1, …, $t9 for temporary values
  $s0, $s1, …, $s7 for saved variables
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
§2.3 Operands of the Computer Hardware
Notes: - Operands of arth instruction are restricted; they must be in from a limited number of locations in hardware called registers
Registers are primitives used in hardware design, also visible to programmer when the computer is completed
MIPS-32 architecture has 32 registers each of size 32-bit
  t0 – t9, s0 – s7 are registers
  t0 – t9 registers used to store temporary values
  s0-s7 registers are for saving variables
Design principle: smaller is faster – MIPS architecture has only 32 registers
  A very large number of registers may increase the clock cycle time simply because it takes electronic signals longer when they must travel farther.
  But main memory has millions of locations
Tradeoff #registers vs clock cycle time

## Slide 7: Register Operand Example
C code:
f = (g + h) - (i + j);
  f, …, j in $s0, …, $s4
Compiled MIPS code:
add $t0, $s1, $s2 add $t1, $s3, $s4 sub $s0, $t0, $t1
Notes: - It is the compiler’s job to associate program variables with registers.
- The variables f, g, h, i, and j are assigned to the registers $s0, $s1, $s2, $s3, and $s4, respectively.
- What is the compiled MIPS code?
- Same as previous, replace the variables with the register names mentioned above plus two temporary registers, $t0 and $t1

## Slide 8: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words are aligned in memory
  Address must be a multiple of 4
MIPS is Big Endian
  Most-significant byte at least address of a word
  c.f. Little Endian: least-significant byte at least address
Notes: - - It is the compiler’s job to allocate data structures to locations in memory.

## Slide 9: Memory Operand Example 1
C code:
g = h + A[8];
  g in $s1, h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
    4 bytes per word
lw $t0, 32($s3) # load word add $s1, $s2, $t0
offset
base register

## Slide 10: Memory Operand Example 2
C code:
A[12] = h + A[8];
  h in $s2, base address of A in $s3
Compiled MIPS code:
  Index 8 requires offset of 32
lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word

## Slide 11: Registers vs. Memory
Registers are faster to access than memory
Operating on memory data requires loads and stores
  More instructions to be executed
Compiler must use registers for variables as much as possible
  Only spill to memory for less frequently used variables
  Register optimization is important!
Notes: data accesses are faster if data is in registers instead of memory.
Accessing registers also uses less energy than accessing memory.
To achieve highest performance and conserve energy, an instruction set architecture must have a sufficient number of registers, and compilers must use registers efficiently.
A MIPS arithmetic instruction can read two registers, operate on them, and write the result.
A MIPS data transfer instruction only reads one operand or writes one operand, without operating on it.

## Slide 12: Immediate Operands
Constant data specified in an instruction
addi $s3, $s3, 4
No subtract immediate instruction
  Just use a negative constant
  addi $s2, $s1, -1
Design Principle 3: Make the common case fast
  Small constants are common
  Immediate operand avoids a load instruction
Notes: - more than half of the MIPS arithmetic instructions have a constant as an operand when running the SPEC CPU2006 benchmarks - Common
- Using only the instructions we have seen so far, we would have to load a constant from memory to use one. (The constants would have been placed in memory when the program was loaded.)
An alternative that avoids the load instruction is to offer versions of the arithmetic instructions in which one operand is a constant. This quick add instruction with one constant operand is called add immediate or addi.
by including constants inside arithmetic instructions, operations are much faster and use less energy than if constants were loaded from memory.

## Slide 13: The Constant Zero
MIPS register 0 ($zero) is the constant 0
  Cannot be overwritten
Useful for common operations
  E.g., move between registers
  add $t2, $s1, $zero
Notes: Given the importance of registers, what is the rate of increase in the number of registers in a chip over time?
Very fast: They increase as fast as Moore’s law, which predicts doubling the number of transistors on a chip every 18 months.
Very slow: Since programs are usually distributed in the language of the computer, there is inertia in instruction set architecture, and so the number of registers increases only as fast as new instruction sets become viable.

## Slide 14: Unsigned Binary Integers
Given an n-bit number
Range: 0 to +2n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 10112 = 0 + … + 1×23 + 0×22 +1×21 +1×20 = 0 + … + 8 + 0 + 2 + 1 = 1110
Using 32 bits
  0 to +4,294,967,295
§2.4 Signed and Unsigned Numbers
Notes: Just as base 10 numbers are called decimal numbers, base 2 numbers are called binary numbers
Numbers are kept in computer hardware as a series of high and low electronic signals, and so they are considered base 2 numbers.
Generalizing the point, in any number base, the value of i th digit d is d x Base ^ i - where i starts at 0 and increases from right to left.
Since words are drawn vertically as well as horizontally, leftmost and rightmost may be unclear. Hence, the phrase least significant bit is used to refer to the right- most bit (bit 0 above) and most significant bit to the leftmost bit (bit 31).
The MIPS word is 32 bits long, so we can represent 232 different 32-bit patterns. It is natural to let these combinations represent the numbers from 0 to 232 􏰂1

## Slide 15: 2s-Complement Signed Integers
Given an n-bit number
Range: –2n – 1 to +2n – 1 – 1
Example
  1111 1111 1111 1111 1111 1111 1111 11002 = –1×231 + 1×230 + … + 1×22 +0×21 +0×20 = –2,147,483,648 + 2,147,483,644 = –410
Using 32 bits
  –2,147,483,648 to +2,147,483,647
Notes: 0000 0000 0000 0000 0000 0000 0000 0000 = 0
0000 0000 0000 0000 0000 0000 0000 0001 = 1ten
0000 0000 0000 0000 0000 0000 0000 0010 = 2ten
... 0111 1111 1111 1111 1111 1111 1111 1101= 2,147,483,645
0111 1111 1111 1111 1111 1111 1111 1110 = 2,147,483,646
0111 1111 1111 1111 1111 1111 1111 1111 = 2,147,483,647
1000 0000 0000 0000 0000 0000 0000 0000 = 2,147,483,648
1000 0000 0000 0000 0000 0000 0000 0001 = 2,147,483,647
1000 0000 0000 0000 0000 0000 0000 0010 = 2,147,483,646
…. 1111 1111 1111 1111 1111 1111 1111 1101 = -3
1111 1111 1111 1111 1111 1111 1111 1110 = -2
1111 1111 1111 1111 1111 1111 1111 1111 = -1

## Slide 16: 2s-Complement Signed Integers
Bit 31 is sign bit
  1 for negative numbers
  0 for non-negative numbers
–(–2n – 1) can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000
  Most-positive: 0111 1111 … 1111
Notes: leading 0s mean positive, and leading 1s mean negative.
This convention for representing signed binary numbers is called two’s complement representation

## Slide 17: Signed Negation
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 00102
  –2 = 1111 1111 … 11012 + 1 = 1111 1111 … 11102
Notes: we need to represent both positive and negative integers within a computer word

## Slide 18: Representing Instructions
Instructions are encoded in binary
  Called machine code
MIPS instructions
  Encoded as 32-bit instruction words
  Small number of formats encoding operation code (opcode), register numbers, …
  Regularity!
Register numbers
  $t0 – $t7 are reg’s 8 – 15
  $t8 – $t9 are reg’s 24 – 25
  $s0 – $s7 are reg’s 16 – 23
§2.5 Representing Instructions in the Computer
Notes: - We are now ready to explain the difference between the way humans instruct computers and the way computers see instructions.
Instructions are kept in the computer as a series of high and low electronic signals and may be represented as numbers. In fact, each piece of an instruction can be considered as an individual number, and placing these numbers side by side forms the instruction.
Since registers are referred to in instructions, there must be a convention to map register names into numbers. In MIPS assembly language, registers $s0 to $s7 map onto registers 16 to 23, and registers $t0 to $t7 map onto registers 8 to 15. Hence, $s0 means register 16, $s1 means register 17, $s2 means register 18, . . . , $t0 means register 8, $t1 means register 9, and so on.

## Slide 19: MIPS R-format Instructions
Instruction fields
  op: operation code (opcode)
  rs: first source register number
  rt: second source register number
  rd: destination register number
  shamt: shift amount (00000 for now)
  funct: function code (extends opcode)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: This layout of the instruction is called the instruction format. As you can see from counting the number of bits, this MIPS instruction takes exactly 32 bits—the same size as a data word. In keeping with our design principle that simplicity favors regularity, all MIPS instructions are 32 bits long
Here is the meaning of each name of the fields in MIPS instructions:
■ op: Basic operation of the instruction, traditionally called the opcode.
■ rs: The first register source operand.
■ rt: The second register source operand.
■ rd: The register destination operand. It gets the result of the operation.
■ shamt: Shift amount. (I will explaing why the field contains zero later.)
■ funct: Function. This field, often called the function code, selects the specific variant of the operation in the op field.

## Slide 20: R-format Example
add $t0, $s1, $s2
special
$s1
$s2
$t0
0
add
0
17
18
8
0
32
000000
10001
10010
01000
00000
100000
000000100011001001000000001000002 = 0232402016
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: We’ll show the real MIPS language version of the instruction represented symbolically as
add $t0,$s1,$s2  assembly language
first as a combination of decimal numbers and then of binary numbers.
The decimal representation is
Each of these segments of an instruction is called a field. The first and last fields (containing 0 and 32 in this case) in combination tell the MIPS computer that this instruction performs addition. The second field gives the number of the register that is the first source operand of the addition operation (17 = $s1), and the third field gives the other source operand for the addition (18 􏰁 $s2). The fourth field contains the number of the register that is to receive the sum (8 = $t0). The fifth field is unused in this instruction, so it is set to 0. Thus, this instruction adds register $s1 to register $s2 and places the sum in register $t0.
This instruction can also be represented as fields of binary numbers as opposed to decimal, as shown above.
To distinguish it from assembly language, we call the numeric version of instructions machine language and a sequence of such instructions machine code.

## Slide 21: Hexadecimal
Base 16
  Compact representation of bit strings
  4 bits per hex digit
0 | 0000 | 4 | 0100 | 8 | 1000 | c | 1100
1 | 0001 | 5 | 0101 | 9 | 1001 | d | 1101
2 | 0010 | 6 | 0110 | a | 1010 | e | 1110
3 | 0011 | 7 | 0111 | b | 1011 | f | 1111
Example: eca8 6420
  1110 1100 1010 1000 0110 0100 0010 0000
Notes: It would appear that you would now be reading and writing long, tedious strings of binary numbers. We avoid that tedium by using a higher base than binary that converts easily into binary. Since almost all computer data sizes are multiples of 4, hexadecimal (base 16) numbers are popular. Since base 16 is a power of 2, we can trivially convert by replacing each group of four binary digits by a single hexadecimal digit, and vice versa.
the table converts between hexadecimal and binary.

## Slide 22: MIPS I-format Instructions
Immediate arithmetic and load/store instructions
  rt: destination or source register number
  Constant: –215 to +215 – 1
  Address: offset added to base address in rs
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible
op
rs
rt
constant or address
6 bits
5 bits
5 bits
16 bits
Notes: The compromise chosen by the MIPS designers is to keep all instructions the same length, thereby requiring different kinds of instruction formats for different kinds of instructions. For example, the format we looked at so far is called R-type (for register) or R-format.
A second type of instruction format shown here is called I-type (for immediate) or I-format and is used by the immediate and data transfer instructions. The fields of I-format are op (6bits), rs (5bits), rt(5bits), constant or address (16bits)
g = h + A[8]; . lw $t0,32($s3) # Temporary reg $t0 gets A[8]
The 16-bit address means a load word instruction can load any word within a region of + or – 2^15 or 32,768 bytes (+or- 2^13 or 8192 words) of the address in the base register rs
Here, 19 (for $s3) is placed in the rs field, 8 (for $t0) is placed in the rt field, and 32 is placed in the address field. Note that the meaning of the rt field has changed for this instruction: in a load word instruction, the rt field specifies the destination register, which receives the result of the load.
Although multiple formats complicate the hardware, we can reduce the complexity by keeping the formats similar. For example, the first three fields of the R-type and I-type formats are the same size and have the same names; the length of the fourth field in I-type is equal to the sum of the lengths of the last three fields of R-type.

## Slide 23: MIPS Instruction encoding
Notes: In the table above, “reg” means a register number between 0 and 31, “address” means a 16-bit address, and “n.a.” (not applicable) means this field does not appear in this format. Note that add and sub instructions have the same value in the op field; the hardware uses the funct field to decide the variant of the operation: add (32) or subtract (34).
The desire to keep all instructions the same size is in conflict with the desire to have as many registers as possible. Any increase in the number of registers uses up at least one more bit in every register field of the instruction format. Given these constraints and the design princple that smaller is faster, most instruction sets today have 16 or 32 general purpose registers.

## Slide 24: MIPS machine language
Notes: The two MIPS instruction formats so far are R and I. The first 16 bits are the same: both contain an op field, giving the base operation; an rs field, giving one of the sources; and the rt field, which specifies the other source operand, except for load word, where it specifies the destination register. R-format divides the last 16 bits into an rd field, specifying the destination register; the shamt field, which we explain it later; and the funct field, which specifies the specific operation of R-format instructions. I-format combines the last 16 bits into a single address field.
Today’s computers are built on two key principles:
Instructions are represented as numbers.
Programs are stored in memory to be read or written, just like data.

## Slide 25: Stored Program Computers
Instructions represented in binary, just like data
Instructions and data stored in memory
Programs can operate on programs
  e.g., compilers, linkers, …
Binary compatibility allows compiled programs to work on different computers
  Standardized ISAs
The BIG Picture
Notes: The stored-program concept. Stored programs allow a computer that performs accounting to become, in the blink of an eye, a computer that helps an author write a book. The switch happens simply by loading memory with programs and data and then telling the computer to begin executing at a given location in memory. Treating instructions in the same way as data greatly simplifies both the memory hardware and the software of computer systems. Specifically, the memory technology needed for data can also be used for programs, and programs like compilers, for instance, can translate code written in a notation far more convenient for humans into code that the computer can understand.
shows the power of the concept; Imagine you are writing a ‘c’ program using an editor (gedit, vim). Here memory can contain the source code for an editor program, the corresponding compiled machine code of editor program, the text that the compiled program is using, and even the compiler that generated the machine code from ‘C’ program.
One consequence of instructions as numbers is that programs are often shipped as files of binary numbers. The commercial implication is that computers can inherit ready-made software provided they are compatible with an existing instruction set. Such “binary compatibility” often leads industry to align around a small number of instruction set architectures.

## Slide 26: Logical Operations
Instructions for bitwise manipulation
Operation | C | Java | MIPS
Shift left | << | << | sll
Shift right | >> | >>> | srl
Bitwise AND | & | & | and, andi
Bitwise OR | ¦ | ¦ | or, ori
Bitwise NOT | ~ | ~ | nor
Useful for extracting and inserting groups of bits in a word
§2.6 Logical Operations

## Slide 27: Shift Operations
shamt: how many positions to shift
Shift left logical
  Shift left and fill with 0 bits
  sll by i bits multiplies by 2i
Shift right logical
  Shift right and fill with 0 bits
  srl by i bits divides by 2i (unsigned only)
op
rs
rt
rd
shamt
funct
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits

## Slide 28: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0000 1100 0000 0000
$t0

## Slide 29: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or $t0, $t1, $t2
0000 0000 0000 0000 0000 1101 1100 0000
0000 0000 0000 0000 0011 1100 0000 0000
$t2
$t1
0000 0000 0000 0000 0011 1101 1100 0000
$t0

## Slide 30: NOT Operations
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
MIPS has NOR 3-operand instruction
  a NOR b == NOT ( a OR b )
nor $t0, $t1, $zero
0000 0000 0000 0000 0011 1100 0000 0000
$t1
1111 1111 1111 1111 1100 0011 1111 1111
$t0
Register 0: always read as zero

## Slide 31: Conditional Operations
Branch to a labeled instruction if a condition is true
  Otherwise, continue sequentially
beq rs, rt, L1
  if (rs == rt) branch to instruction labeled L1;
bne rs, rt, L1
  if (rs != rt) branch to instruction labeled L1;
j L1
  unconditional jump to instruction labeled L1
§2.7 Instructions for Making Decisions

## Slide 32: Compiling If Statements
C code:
if (i==j) f = g+h; else f = g-h;
  f, g, … in $s0, $s1, …
Compiled MIPS code:
bne $s3, $s4, Else add $s0, $s1, $s2 j Exit Else: sub $s0, $s1, $s2 Exit: …
Assembler calculates addresses

## Slide 33: Compiling Loop Statements
C code:
while (save[i] == k) i += 1;
  i in $s3, k in $s5, address of save in $s6
Compiled MIPS code:
Loop: sll $t1, $s3, 2 add $t1, $t1, $s6 lw $t0, 0($t1) bne $t0, $s5, Exit addi $s3, $s3, 1 j Loop Exit: …

## Slide 34: Basic Blocks
A basic block is a sequence of instructions with
  No embedded branches (except at end)
  No branch targets (except at beginning)
A compiler identifies basic blocks for optimization
An advanced processor can accelerate execution of basic blocks

## Slide 35: More Conditional Operations
Set result to 1 if a condition is true
  Otherwise, set to 0
slt rd, rs, rt
  if (rs < rt) rd = 1; else rd = 0;
slti rt, rs, constant
  if (rs < constant) rt = 1; else rt = 0;
Use in combination with beq, bne
  slt $t0, $s1, $s2 # if ($s1 < $s2) bne $t0, $zero, L # branch to L

## Slide 36: Branch Instruction Design
Why not blt, bge, etc?
Hardware for <, ≥, … slower than =, ≠
  Combining with branch involves more work per instruction, requiring a slower clock
  All instructions penalized!
beq and bne are the common case
This is a good design compromise

## Slide 37: Signed vs. Unsigned
Signed comparison: slt, slti
Unsigned comparison: sltu, sltui
Example
  $s0 = 1111 1111 1111 1111 1111 1111 1111 1111
  $s1 = 0000 0000 0000 0000 0000 0000 0000 0001
  slt $t0, $s0, $s1 # signed
    –1 < +1  $t0 = 1
  sltu $t0, $s0, $s1 # unsigned
    +4,294,967,295 > +1  $t0 = 0

## Slide 38: Procedure Calling
Steps required
  Place parameters in registers
  Transfer control to procedure
  Acquire storage for procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call
§2.8 Supporting Procedures in Computer Hardware
Notes: A procedure or function is one tool programmers use to structure programs, both to make them easier to understand and to allow code to be reused. Procedures allow the programmer to concentrate on just one portion of the task at a time; parameters act as an interface between the procedure and the rest of the program and data, since they can pass values and return results.
You can think of a procedure like a spy who leaves with a secret plan, acquires resources, performs the task, covers his or her tracks, and then returns to the point of origin with the desired result.
Similarly, in the execution of a procedure, the program must follow these six steps:
1. Put parameters in a place where the procedure can access them.
2. Transfer control to the procedure.
3. Acquire the storage resources needed for the procedure.
4. Perform the desired task.
5. Put the result value in a place where the calling program can access it.
6. Return control to the point of origin, since a procedure can be called from several points in a program.

## Slide 39: Register Usage
$a0 – $a3: arguments (reg’s 4 – 7)
$v0, $v1: result values (reg’s 2 and 3)
$t0 – $t9: temporaries
  Can be overwritten by callee
$s0 – $s7: saved
  Must be saved/restored by callee
$gp: global pointer for static data (reg 28)
$sp: stack pointer (reg 29)
$fp: frame pointer (reg 30)
$ra: return address (reg 31)
Notes: MIPS software follows the following convention for procedure calling in allocating its 32 registers:
■ $a0–$a3: four argument registers in which to pass parameters
■ $v0–$v1: two value registers in which to return values ■ $ra: one return address register to return to the point of origin

## Slide 40: Procedure Call Instructions
Procedure call: jump and link
jal ProcedureLabel
  Address of following instruction put in $ra
  Jumps to target address
Procedure return: jump register
jr $ra
  Copies $ra to program counter
  Can also be used for computed jumps
    e.g., for case/switch statements
Notes: Imaging a ‘C’ code
f()
{
statement A
statement B
return
}
main()
{
statement w
statement x
f()
statement y
statement z
….
}
Imagine the following instructions in a main function:
inst w
inst x
jump procedurelabel
inst y
inst z
..
..
procedurelabel: inst A
inst B
..
..
..
go back to inst z
How to go back to main and execute remaining instructions in main() function, that is from statement z to the end.
answer is jal ProcedureAddress  MIPS assembly language includes jal instruction just for the procedures: jal jumps to an address and simultaneously saves the address of the following instruction in register $ra.
Here the following instruction has inst y. So $ra is loaded with the address of inst y.
Now, before exit the procedure call unconditional jump to location in $ra using jr $ra instruction.
Note, processor has a special register called programcounter (PC), which has address to the instruction that should be executed.
The jal instruction actually saves PC+4 in register $ra to link to the following instruction to set up the procedure return.
So jr $ra copies address of inst y to PC.

## Slide 41: Leaf Procedure Example
C code:
int leaf_example (int g, h, i, j) { int f; f = (g + h) - (i + j); return f; }
  Arguments g, …, j in $a0, …, $a3
  f in $s0 (hence, need to save $s0 on stack)
  Result in $v0
Notes: Suppose a compiler needs more registers for a procedure than the four argument and two return value registers. Since we must cover our tracks after our mission is complete, any registers needed by the caller must be restored to the values that they contained before the procedure was invoked. This situation is an example in which we need to spill registers to memory.
The ideal data structure for spilling registers is a stack—a last-in-first-out queue. A stack needs a pointer to the most recently allocated address in the stack to show where the next procedure should place the registers to be spilled or where old register values are found. The stack pointer is adjusted by one word for each register that is saved or restored. MIPS software reserves register 29 for the stack pointer, giving it the obvious name $sp. Stacks are so popular that they have their own buzzwords for transferring data to and from the stack: placing data onto the stack is called a push, and removing data from the stack is called a pop.
By historical precedent, stacks “grow” from higher addresses to lower addresses. This convention means that you push values onto the stack by subtracting from the stack pointer. Adding to the stack pointer shrinks the stack, thereby popping values off the stack.
The parameter variables g, h, i, and j correspond to the argument registers $a0, $a1, $a2, and $a3, and f corresponds to $s0, result of leaf_example in $v0

## Slide 42: Leaf Procedure Example
MIPS code:
leaf_example: addi $sp, $sp, -4 sw $s0, 0($sp) add $t0, $a0, $a1 add $t1, $a2, $a3 sub $s0, $t0, $t1 add $v0, $s0, $zero lw $s0, 0($sp) addi $sp, $sp, 4 jr $ra
Save $s0 on stack
Procedure body
Restore $s0
Result
Return
Notes: leaf_example:
1. The next step is to save the registers used by the procedure. We save $s0 value onto the stack by creating space for a word (4 bytes) on the stack and then store them.
2. The next three statements correspond to the body of the procedure
3. To return the value of f (s0) we copy it into a return value register $v0
4. Before returning, we restore the old value of s0 register we saved by “popping” it from the stack
5. The procedure ends with a jump register using the return address:
Stackpointer (sp) itself preserved by the callee adding exactly the same amount (+4) that was subtracted from it (-4); and the other registers (sw s0) are preserved by saving them on the stack (if they are used) and restoring them from there (lw s0).

## Slide 43: Non-Leaf Procedures
Procedures that call other procedures
For nested call, caller needs to save on the stack:
  Its return address
  Any arguments and temporaries needed after the call
Restore from the stack after the call
Notes: Procedures that do not call others are called leaf procedures. Life would be simple if all procedures were leaf procedures, but they aren’t. Just as a spy might employ other spies as part of a mission, who in turn might use even more spies, so do procedures invoke other procedures. Moreover, recursive procedures even invoke “clones” of themselves. Just as we need to be careful when using registers in procedures, more care must also be taken when invoking nonleaf procedures.
For example, suppose that the main program calls procedure A with an argument of 3, by placing the value 3 into register $a0 and then using jal A. Then suppose that procedure A calls procedure B via jal B with an argument of 7, also placed in $a0. Since A hasn’t finished its task yet, there is a conflict over the use of register $a0. Similarly, there is a conflict over the return address in register $ra, since it now has the return address for B. Unless we take steps to prevent the problem, this conflict will eliminate procedure A’s ability to return to its caller.
One solution is to push all the other registers that must be preserved onto the stack, just as we did with the saved registers (s0).

## Slide 44: Non-Leaf Procedure Example
C code:
int fact (int n) { if (n < 1) return 1; else return n * fact(n - 1); }
  Argument n in $a0
  Result in $v0
Notes: Let’s tackle a recursive procedure that calculates factorial:
What is the MIPS assembly code?

## Slide 45: Non-Leaf Procedure Example
MIPS code:
fact: addi $sp, $sp, -8 # adjust stack for 2 items sw $ra, 4($sp) # save return address sw $a0, 0($sp) # save argument slti $t0, $a0, 1 # test for n < 1 beq $t0, $zero, L1 addi $v0, $zero, 1 # if so, result is 1 addi $sp, $sp, 8 # pop 2 items from stack jr $ra # and return L1: addi $a0, $a0, -1 # else decrement n jal fact # recursive call lw $a0, 0($sp) # restore original n lw $ra, 4($sp) # and return address addi $sp, $sp, 8 # pop 2 items from stack mul $v0, $a0, $v0 # multiply to get result jr $ra # and return
Notes: 1. The parameter variable n corresponds to the argument register $a0. The compiled program starts with the label of the procedure and then saves two registers on the stack, the return address and $a0
2. The first time fact is called, sw saves an address in the program that called fact. The next two instructions test whether n is less than 1, going to L1 if n ≥ 1.
3. If n is less than 1, fact returns 1 by putting 1 into a value register: it adds 1 to 0 and places that sum in $v0. It then pops the two saved values off the stack and jumps to the return address
4. Before popping two items off the stack, we could have loaded $a0 and $ra. Since $a0 and $ra don’t change when n is less than 1, we skip those instructions. If n is not less than 1, the argument n is decremented and then fact is called again with the decremented value
5. The next instruction is where fact returns. Now the old return address and old argument are restored, along with the stack pointer
6. Next, the value register $v0 gets the product of old argument $a0 and the current value of the value register. We assume a multiply instruction is available, even though it is not covered until Chapter 3
7. Finally, fact jumps again to the return address

## Slide 46: Local Data on the Stack
Local data allocated by callee
  e.g., C automatic variables
Procedure frame (activation record)
  Used by some compilers to manage stack storage
Notes: Local/automatic variables - Automatic variables are local to a procedure and are discarded when the procedure exits.
Static variables - C variables declared outside all procedures are considered static. Static variables exist across exits from and entries to procedures.
The segment of the stack containing a procedure’s saved registers and local variables is called a procedure frame or activation record.
Some MIPS software uses a frame pointer ($fp) to point to the first word of the frame of a procedure. A stack pointer might change during the procedure, and so references to a local variable in memory might have different offsets depending on where they are in the procedure, making the procedure harder to understand. Alternatively, a frame pointer offers a stable base register within a procedure for local memory-references.

## Slide 47: Memory Layout
Text: program code
Static data: global variables
  e.g., static variables in C, constant arrays and strings
  $gp initialized to address allowing ±offsets into this segment
Dynamic data: heap
  E.g., malloc in C, new in Java
Stack: automatic storage
Notes: The figure shows the MIPS convention for allocation of memory.
The first part of the low end of memory is reserved, followed by the home of the MIPS machine code, traditionally called the text segment. the program code (“text”) starts at 0040 0000_hex.
Above the code is the static data segment, which is the place for constants, constant arrays, strings, and other static variables. arrays tend to be a fixed length and thus are a good match to the static data segment. The static data starts at 1000 0000_hex. The global pointer, $gp, is set to an address to make it easy to access data. It is initialized to 1000 8000_hex so that it can access from 1000 0000_hex to 1000 ffff_hex using the positive and negative 16-bit offsets from $gp.
However, data structures like linked lists tend to grow and shrink during their lifetimes. The segment for such data structures is traditionally called the heap, and it is placed next in memory. Dynamic data, allocated by malloc in C and by new in Java,
C allocates and frees space on the heap with explicit functions. malloc() allocates space on the heap and returns a pointer to it, and free() releases space on the heap to which the pointer points.
The stack starts in the high end of memory and grows down. The stack pointer is initialized to 7fff fffc_hex and grows down toward the data segment.
Note that this allocation allows the stack and heap to grow toward each other, thereby allowing the efficient use of memory as the two segments wax and wane.

## Slide 48: Byte/Halfword Operations
Byte-encoded character sets
  ASCII: 128 characters (95 graphic, 33 control)
Could use bitwise operations
MIPS byte/halfword load/store
  String processing is a common case
lb rt, offset(rs) lh rt, offset(rs)
  Sign extend to 32 bits in rt
lbu rt, offset(rs) lhu rt, offset(rs)
  Zero extend to 32 bits in rt
sb rt, offset(rs) sh rt, offset(rs)
  Store just rightmost byte/halfword
Notes: Computers were invented to crunch numbers, but as soon as they became commercially viable they were used to process text. Most computers today offer 8-bit bytes to represent characters, with the American Standard Code for Information Interchange (ASCII) being the representation
A series of bitwise instructions can extract a byte from a word, so load word and store word are sufficient for transferring bytes as well as words.
Because of the popularity of text in some programs, however, MIPS provides instructions to move bytes.
  Load byte (lb) loads a byte from memory, placing it in the rightmost 8 bits of a register.
  Store byte (sb) takes a byte from the rightmost 8 bits of a register and writes it to memory.
lb – copies sign bit (0/1) in the most significant bit, make 24 copies, and place the sign (0/1) in the left-hand (24 bits) of the word (rt)
lbu - makes 24 copies of 0, and place 0 in the left-hand (24 bits) of the word (rt)

## Slide 49: String Copy Example
C code (naïve):
  Null-terminated string
void strcpy (char x[], char y[]) { int i; i = 0; while ((x[i]=y[i])!='\0') i += 1; }
  Addresses of x, y in $a0, $a1
  i in $s0
Notes: - Characters are normally combined into strings, which have a variable number of characters.
There are three choices for representing a string: (1) the first position of the string is reserved to give the length of a string, (2) an accompanying variable has the length of the string (as in a structure), or (3) the last position of a string is indicated by a character used to mark the end of a string.
C uses the third choice, terminating a string with a byte whose value is 0 (named null in ASCII). Thus, the string “Cal” is represented in C by the following 4 bytes, shown as decimal numbers: 67, 97, 108, 0. (As we shall see, Java uses the first option.)

## Slide 50: String Copy Example
MIPS code:
strcpy: addi $sp, $sp, -4 # adjust stack for 1 item sw $s0, 0($sp) # save $s0 add $s0, $zero, $zero # i = 0 L1: add $t1, $s0, $a1 # addr of y[i] in $t1 lbu $t2, 0($t1) # $t2 = y[i] add $t3, $s0, $a0 # addr of x[i] in $t3 sb $t2, 0($t3) # x[i] = y[i] beq $t2, $zero, L2 # exit loop if y[i] == 0 addi $s0, $s0, 1 # i = i + 1 j L1 # next iteration of loop L2: lw $s0, 0($sp) # restore saved $s0 addi $sp, $sp, 4 # pop 1 item from stack jr $ra # and return
Notes: - Note that we don’t have to multiply i by 4 since y is an array of bytes and not of words, as in prior examples.
-